## Slide 1: Interpreting fine particulate matter (PM2.5) trends in South Korea, 2011-2022 Drew Pendergrass | AMS Annual Meeting January 14, 2025 with Daniel J. Jacob, Yujin J. Oak, Ruijun Dang, Laura Hyesung Yang, Ellie Beaudry, Nadia K. Colombi, Shixian Zhai, Hwajin Kim, Jin-soo Choi, Jin-soo Park, Soontae Kim, and Hong Liao

## Slide 2: Table of contents
Producing a unified national PM2.5 dataset for South Korea
Three distinct periods of PM2.5 behavior:
Transition 2: Changes in particulate nitrate
Transition 1: Evidence from the weekend effect
Conclusions
2011-2014
2015-2018
2019-2022
Transition 1
Transition 2

## Slide 3: Table of contents
Producing a unified national PM2.5 dataset for South Korea
Three distinct periods of PM2.5 behavior:
Transition 2: Changes in particulate nitrate
Transition 1: Evidence from the weekend effect
Conclusions
2011-2014
2015-2018
2019-2022
Transition 1
Transition 2

## Slide 4: PM2.5 surface stations were deployed across South Korea in 2015, missing key events
China: Action Plan on Prevention and Control of Air Pollution
2012 2013 2014 2015 2016 2017 2018 2019 2020 2021 2022
Korea: Comprehensive Action Plan on Fine Dust
2016 obs.
2022 obs.
2019 obs.
100
80
60
50
40
30
20
10
8
6
5
4
PM2.5 (µg m-3)
Seoul: seasonal fine dust management program (Dec.-Mar.)
2013 obs.
Region: Covid lockdowns
Seoul had its own network before 2015
10
20
30
40
Annual PM2.5 (µg m-3)
Notes: No before and after for Korea or China with 2013 action plan – most impactful policy. Can’t compare to impacts of 2017 policy.

## Slide 5: However, AirKorea network measured PM10, O3, NO2, CO, and SO2 before 2015
Infer with random forest
Observed PM10

## Slide 6: PM10 by far most important predictor for PM2.5 at AirKorea sites, followed by CO and humidity
RF Shapley analysis (less impt. variables not shown)

## Slide 7: AirKorea RF PM2.5 performs well in 2015-20 training period and has only modest bias against separate 2011-15 Seoul municipal PM2.5 dataset
Pure extrapolation! We do not use Seoul PM2.5 data for training.

## Slide 8: Table of contents
Producing a unified national PM2.5 dataset for South Korea
Three distinct periods of PM2.5 behavior:
Transition 2: Changes in particulate nitrate
Transition 1: Evidence from the weekend effect
Conclusions
2011-2014
2015-2018
2019-2022
Transition 1
Transition 2

## Slide 9: We find PM2.5 decreases everywhere, after controlling for meteorology using multi-linear regression
Met-normalized
PM2.5 trend
2011-22
MLR R2
2011-22
0.45
0.40
0.35
0.30
0.25
-6
-4
-2
0
2
4
6
∆PM2.5 (µg m-3 a-1)
R2
Notes: Aggregate sites to 0.25 grid and detrend
Use MLR to fit PM2.5 to top three met variables (by AIC) to make met model
  Variables considered are: boundary layer height, sea level pressure, precip, surface RH, surface T, 10m wind speed, meridional (v) winds at 850 hPa
Remove met fit; residuals plotted.

## Slide 10: Overall decrease obscures three distinct periods of PM2.5 behavior

## Slide 11: Table of contents
Producing a unified national PM2.5 dataset for South Korea
Three distinct periods of PM2.5 behavior:
Transition 2: Changes in particulate nitrate
Transition 1: Evidence from the weekend effect
Conclusions
2011-2014
2015-2018
2019-2022
Transition 1
Transition 2

## Slide 12: Particulate nitrate (pNO3-) drives DJF increases for 2015–2019 and decreases for 2019–2022
Seoul obs.
DJF
Baengnyeong
obs.
DJF
Baeng.
Seoul
2
3
2
3

## Slide 13: pNO3- in Korea can be limited by NO or NH3 emissions depending on ambient conditions
HNO3
NO
NO2
hv
O3, peroxy
Fuels, soil
PM2.5 nitrate
NH4+ + NO3-
Oxidation
Thermodynamic partitioning
NH3
agriculture, vehicles
T RH
Slide adapted from Ruijun Dang
Coal
SO2
H2SO4
NH3
2NH4+ + SO42-
PM2.5 sulfate
OH
Notes: SO2 down, so in transitional phase more NH3 available to form particulate nitrate and more mass in particle phase.

## Slide 14: Like ozone, pNO3- sensitivity to emissions can be diagnosed from space
Dang et al., 2023
Notes: Say that VOC sensitive regime is not relevant in South Korea at the spatial resolution we consider. Comes up in the North China Plain.

## Slide 15: NH3/NO2 ratio suggests pNO3- has become NOx limited from 2019 in Seoul Metropolitan Area (SMA)
Notes: NH3 has stayed relatively constant, NOx decreasing throughout the study period.

## Slide 16: Table of contents
Producing a unified national PM2.5 dataset for South Korea
Three distinct periods of PM2.5 behavior:
Transition 2: Changes in particulate nitrate
Transition 1: Evidence from the weekend effect
Conclusions
2011-2014
2015-2018
2019-2022
Transition 1
Transition 2

## Slide 17: There is a prominent PM2.5 “weekend effect” and it reverses sign around 2015
Real PM2.5 observations from Seoul network
Daily gap-free 2×2 km2 PM2.5 for all East Asia (used for these plots), available here:

## Slide 18: Secondary nighttime chemistry drives the weekend effect change
Org
NO3-
SO42-
NH4+
BC
Weekday
Weekend
Jan. 2016-18 PM1 composition
Data from Hwajin Kim
Seoul PM2.5 weekday minus weekend
by hour of day (city-wide observations)
More polluted during week
Less polluted during week
∆PM2.5 (µg m-3)
Hour of day
Notes: Before 2015, steady weekend effect throughout day
After 2015, weekend effect driven by nighttime dynamics.
Also note that ozone has increased at all times of day over the study period.

## Slide 19: Secondary nighttime chemistry drives the weekend effect change
Org
NO3-
SO42-
NH4+
BC
Weekday
Weekend
O3
Nighttime O3 titration

## Slide 20: Conclusions
PM2.5 decreases in South Korea from 2011 through 2022, but DJF concentrations increase in the 2015-19 interval.
DJF PM2.5 increased in 2015-19 because of increased nitrate as sulfate declined and ozone increased, then declined as pNO3- production became NOx-limited and responded to emissions cuts.
Since 2015 weekends are more polluted than weekdays in South Korea, reflecting an increasing role for oxidants (secondary PM2.5) as opposed to primary sources.
Nighttime reaction pathways play an important role in the weekend effect and may increase in importance as ozone continues to rise.