## Slide 1: Running CHEEREIO 1.4.1 A hands-on guide to nonlinear ensemble data assimilation and emissions estimation with GEOS-Chem
12th International GEOS-Chem meeting clinic
Drew Pendergrass
June 8, 2026

## Slide 2: Table of contents
Introduction to ensemble data assimilation and CHEEREIO
Installing CHEEREIO and building your first ensemble
Selecting or adding observation operators
Running and debugging CHEEREIO
Postprocessing and data analysis tools

## Slide 3: Table of contents
Introduction to ensemble data assimilation and CHEEREIO
Installing CHEEREIO and building your first ensemble
Selecting or adding observation operators
Running and debugging CHEEREIO
Postprocessing and data analysis tools

## Slide 4: Satellite data can monitor rapidly-changing emissions
Bottom-up emissions estimate
Simulated atmosphere
Real satellite observations
Virtual
observations
Real world
“What if our emissions estimates were correct?”
Pendergrass et al., 2023

## Slide 5: Satellite data can monitor rapidly-changing emissions
Prior emissions estimate
Simulated atmosphere
Real satellite observations
Data-driven emissions
Pendergrass et al., 2023

## Slide 6: The bottom-up method of emissions estimation
Emissions factor
Fuel type, scrubbers, etc.
Vehicle type
Distance traveled
Amount of electricity generated
Activity level
x
=
Emissions
Emissions from electricity
Emissions from transportation
x
x
=
=
+
+
Emissions from other sectors
=
Total emissions
Bottom-up emissions are necessary but imperfect.
Observations can help quantify missing sources.
Notes: Repeat for every pollutant and every source of each pollutant.

## Slide 7: LETKF randomizes emissions and compares model predictions to observations
… satellite would measure 1990 ppb CH4
If we emit 1000 kg CH4 per hour…
If we emit 500 kg CH4 per hour…
… satellite would measure
1980 ppb CH4
Real satellite measures
1985 ppb NOx…
… so truth is in between these two guesses

## Slide 8: How LETKF can estimate emissions of any species
Generate n perturbations
to initial emissions map
…
Run an atmospheric model for each
emission field
…
Generate n simulated 3D atmospheres, each reflecting different emissions
Apply observation operators (e.g. satellite averaging kernels)
Compare simulated observations to actual observations
…
…
Use ensemble spread to approximate prior error covariance matrix
Specify or calculate observational error covariance matrix
Pendergrass et al., 2023
https://cheere.io

## Slide 9
How LETKF can estimate emissions of any species
Weighting by covariance matrices, calculate optimal posterior emissions and/or concentrations
…
…
Generate n simulated 3D atmospheres, each reflecting different emissions
Apply observation operators (e.g. satellite averaging kernels)
Compare simulated observations to actual observations
…
…
Use ensemble spread to approximate prior error covariance matrix
Specify or calculate observational error covariance matrix
Repeat
Run an atmospheric model for each
emission field
Pendergrass et al., 2023
https://cheere.io

## Slide 10: CHEEREIO automates LETKF inversions with state-of-the-science modeling and community tools
From one file…
ens_config.json
Pick your model version and inputs
Standard inputs
Group emissions
Define emissions to optimize
NOx
NO
NO2
Specify uncertainties
Specify observations on disk
Apply filters and real-time corrections
Operator maps data to GEOS-Chem
TROPOMI:
CO, NO2, CH4
IASI:
NH3
CrIS:
Isop.
Any surface data
Community library
Or add with Python
Simulate
Observe

## Slide 11: Past CHEEREIO results: global methane budget
Simulate
Observe
Optimize
Emissions resolved in time…
…and space
Uncertainty
NH3 columns, July 2019
Prior
TROPOMI
Posterior
Northern hemisphere mean methane columns
Pendergrass et al., 2025

## Slide 12: Past CHEEREIO results: understanding sectoral drivers of emissions change
Li et al., in review at ACP
In China, livestock drove the 2019-24 methane emissions increase, more than offsetting coal policy gains

## Slide 13: Past CHEEREIO results: near-real-time monitoring of Canadian wildfires with CO
Voshtani et al., 2025

## Slide 14: Exciting CHEEREIO work in progress
Inverting CO2 fluxes (Yiming Xu and Qianlai Zhuang, Purdue)
Inverting NH3 (IASI) and NOx/SO2 (TROPOMI) (Drew Pendergrass, Duke)
Inverting CrIS VOC products, starting with isoprene and ethane (Dylan Millet and Kelley Wells, UMN)

## Slide 15: Table of contents
Introduction to ensemble data assimilation and CHEEREIO
Installing CHEEREIO and building your first ensemble
Selecting or adding observation operators
Running and debugging CHEEREIO
Postprocessing and data analysis tools

## Slide 16: Getting ready: detailed documentation is provided on ReadTheDocs
All the material discussed today and much more is covered in the CHEEREIO documentation, available at bit.ly/CheereioDocs

## Slide 17: Getting ready: frequently asked questions
How hard is it to run CHEEREIO?
  If your system is set up to run GEOS-Chem Classic, it can run CHEEREIO with a few very minor modifications. User experience is also similar to running GC.
What input data is required for CHEEREIO?
  Same as GEOS-Chem Classic, plus whatever observational data you would like to assimilate (e.g. satellite datasets).
What compute resources are required for CHEEREIO?
  A cluster is necessary. CHEEREIO involves running an ensemble of ~16-48 GEOS-Chem runs simultaneously. Because the calculation is embarrassingly parallel, these runs can be on different nodes or even different partitions (no MPI). Options are available to trade off cores/memory for speed.

## Slide 18: Getting ready: using git to obtain source code
Clone the CHEEREIO repository from GitHub: git clone git@github.com:drewpendergrass/CHEEREIO.git
If you want a CHEEREIO version before the latest release, check out now: git checkout -b NewBranch tags/v1.3.1
Clone the GEOS-Chem Classic repository inside CHEEREIO, or copy GCClassic repo already downloaded.
  git clone --recurse-submodules https://github.com/geoschem/GCClassic.git GCClassic
  This folder must be named GCClassic.
  CHEEREIO works with any version of GEOS-Chem version 13.0.0 or newer.

## Slide 19: Getting ready: setting up software environments
Requirements: GEOS-Chem Classic 13/14 environment, plus
Python as managed by Anaconda or Mamba
jq
Ultra lightweight JSON library for shell. Most clusters have it installed as a module
Parallel
Standard lightweight shell-level parallelization library. Most clusters have it installed as a module

## Slide 20: Getting ready: setting up software environments
Environment file
Conda environments
Modify environments > cheereio.env for your system. This will be your GEOS-Chem environment, plus jq/python/parallel
Install cheereio and animation conda environments (environments > cheereio.yaml and > animation.yml)
Command likely will look like the following:
conda env create -f cheereio.yaml
OR
mamba env create -f cheereio.yaml
Modify CondaEnv and AnimationEnv fields in ens_config.json to match installed environment names (cheereio and animation by default).

## Slide 21: The MOST IMPORTANT PART: editing ens_config.json to define your LETKF problem
All science happens here. Read the documentation first for a line-by-line description.
I recommend starting with one of the supplied templates, using CH4 if you are doing a long-lived species or NH3 if short-lived.
Email me at apenderg@oberlin.edu and I can share state-of-the-science configuration files used by myself or other willing groups.

## Slide 22: Initialization: defining ensemble settings
Ens_config.json supersedes the normal GEOS-Chem run directory creation process.
At the top of the file, you specify your GEOS-Chem settings.
Notes: This is because CHEEREIO manipulates the contents of GC run directories, comprising the ensemble, on the fly.
Don’t worry, you can add more minute adjustements by modifying the template run directory

## Slide 23: Initialization: how should your LETKF start?
Beyond normal spinup, LETKF requires ensemble spinup — time for emissions differences between ensemble members to be realized in concentration spreads.
You set this up in ens_config.json
Concentration
Ensemble of simulations, all starting from same restart
First observations
(Optional) Scale initial ensemble mean to match observation mean, and/or increase ensemble standard deviation
Ensemble spinup
LETKF begins

## Slide 24: Initialization: define the state vector to be optimized
Define state vectors in ens_config.json
Joint optimization of NOx, SO2, and NH3 emissions
Optimize both CH4 concentrations and emissions

## Slide 25
Initialization: tell CHEEREIO how to load the observations you use
We want to jointly assimilate NOx, SO2, and NH3
We will constrain emissions using TROPOMI observations of NO2 and SO2, and IASI observations of NH3
CHEEREIO will look for operational products at these file locations

## Slide 26: Key data assimilation idea: an observation operator transforms GC output so that it can be compared to an observation
GEOS-Chem output is on a grid
Satellites get e.g. a column mixing ratio with varying sensitivities
operators.json
The OBS_TYPE argument tells CHEEREIO which observation operator to use to load your observations

## Slide 27: Initialization: tell CHEEREIO how to load the observations you use
Within the configuration file…
…turn on two observers of one species (CH4)…
TROPOMI
Surface
…turn on TROPOMI for LETKF updates
…but use ObsPack as an independent validation set (no assimilation)
Notes: What’s great about this is that any CHEEREIO observation operator can automatically be used to validate a run, no programming required.

## Slide 28: Initialization: deploying the ensemble
Activate cheereio shell environment
In setup_ensemble.sh turn on Template Run directory creation only
Execute script, then navigate to MY_PATH/RUN_NAME
Copy of code used to run ensemble
Ensemble GC run directories
Postprocessed output files
Temporary files, runtime status
Template GC run directory

## Slide 29: Initialization: deploying the ensemble
Edit template run directory. Settings will be repeated across the ensemble.
CHEEREIO automatically edits HEMCO_Config to link emissions to LETKF scale factors

## Slide 30: Initialization: deploying the ensemble
Return to setup_ensemble.sh
In setup_ensemble.sh turn off Template Run directory creation and turn on compilation and setup ensemble runs.
Execute. We are now ready to run the ensemble!

## Slide 31: Table of contents
Introduction to ensemble data assimilation and CHEEREIO
Installing CHEEREIO and building your first ensemble
Selecting or adding observation operators
Running and debugging CHEEREIO
Postprocessing and data analysis tools

## Slide 32: Add new observation operators easily with Python-based inheritance
CHEEREIO is assembled from interchangeable blocks
Observation operators go here
CHEEREIO provides a template for observation operators…

## Slide 33: Add new observation operators easily with Python-based inheritance
CHEEREIO is assembled from interchangeable blocks
CHEEREIO provides a template for observation operators…
…that then automatically plug in to the CHEEREIO workflow
OMI
TROPOMI
GEMS
Surface
Add your own!
GEMS inversion ready to go!

## Slide 34: Anatomy of a CHEEREIO observation operator
A Python class which inherits the CHEEREIO Observation Translator parent class — templating
(Optional) Utility method that links observer dates to files — speeds up CHEEREIO
(Optional) Obspack-specific method which finds files with observations between two dates

## Slide 35
Anatomy of a CHEEREIO observation operator
Function which loads observation data and saves to a standardized dictionary.
CHEEREIO requires 1D arrays for observer value, longitude, latitude, and utctime. All other fields are optional.
MANDATORY FUNCTION 1
Requires species key (references observed species in ens_config) and time period.

## Slide 36
Anatomy of a CHEEREIO observation operator
MANDATORY FUNCTION 2
Core observation operator which compares GEOS-Chem and observations.
Data is returned in ObsData class, which is a list of 1D arrays where GEOS-Chem data are aligned

## Slide 37: Table of contents
Introduction to ensemble data assimilation and CHEEREIO
Installing CHEEREIO and building your first ensemble
Selecting or adding observation operators
Running and debugging CHEEREIO
Postprocessing and data analysis tools

## Slide 38: Run time: executing the ensemble
(1) Execute nohup bash run_ensspin.sh &
(2) Once all runs complete, execute nohup bash run_ens.sh &

## Slide 39: CHEEREIO runtime: behind the scenes

## Slide 40: Run time: checking ensemble progress, duplication, and backup restoration

## Slide 41: Table of contents
Introduction to ensemble data assimilation and CHEEREIO
Installing CHEEREIO and building your first ensemble
Selecting or adding observation operators
Running and debugging CHEEREIO
Postprocessing and data analysis tools

## Slide 42: Postprocessing: ensemble snapshots and full postprocessing suite
While CHEEREIO is running
Get super-fast view of ensemble status with snapshot.sh

## Slide 43
Hemco output (full emissions, scale factors applied) follows same conventions
Postprocessing: emissions scaling factors

## Slide 44
Postprocessing: bigY, or observation operator raw output
Entries for every assimilation period

## Slide 45
Postprocessing: bigY, or observation operator raw output
For every date, a table of each ensemble mapped to observations, along with geospatial data and metadata

## Slide 46
Postprocessing: bigY, or observation operator raw output
…
For every date, a table of each ensemble mapped to observations, along with geospatial data and metadata

## Slide 47
Postprocessing: bigY gridded for plotting
GC ensemble mean, mapped to operator, gridded (time,lat,lon)
Observations, averaged to GC grid (time,lat,lon)
Control GC simulation, no assimilation (time,lat,lon)
…

## Slide 48: A hopeful promise and a dire warning
Simulate
Observe
Optimize
You can get your first results very fast, from the latest GEOS-Chem or your own custom modification of the code. No new Fortran.
But those first results will be wrong, scientifically. Many adjustments are necessary before errors reduce in a reasonable way.
I am happy to help; send diagnostic plots to apenderg@Oberlin.edu and I can recommend ens_config.json adjustments

## Slide 49
Useful resources
CHEEREIO paper: https://gmd.copernicus.org/articles/16/4793/2023/
CHEEREIO website: https://cheere.io
CHEEREIO documentation: https://cheereio.readthedocs.io
Details on GEOS-Chem (and CHEEREIO) software requirements: https://geos-chem.readthedocs.io/en/stable/getting-started/system-req-soft.html
I am here to help! Ask any questions at https://github.com/drewpendergrass/CHEEREIO/issues (preferred) or by email: apenderg@oberlin.edu